## Slide 1: EEC 134B Proposal 2.4 GHz FMCW Radar System
Team One

## Slide 2: Specification Calculation

## Slide 3: Requirement
Center Frequency: 2.4 GHz
Target size: 0.09 m^2
Maximum target distance: 50 m
Minimum target distance: 5 m
Budget: USD 300

## Slide 4: Power Distribution in RF system
Maximum free space path loss
Patch antenna gain roughly around 4-6 dB
SMA cable loss for 2.4 GHz is 0.9 dB/ft

## Slide 5: Power Distribution in RF system
74.02 dB
0.5 dB
0.5 dB
5 dB
5 dB
-65 dBm
-85 dBm
0 dBm

## Slide 6: Estimate System Performance
Minimum S/N for input of demodulator is set to be 10 dB in our case and NF is 1.44 dB after cascade analysis
The receiver sensitivity is about -85 dBm then we set the margin to 20 dB
From Friis formula, the required transmit power for 50 m target range is

## Slide 7: RF System Block Diagram
RX Total Gain: 6.8 Total NF: 1.44
Sensitivity: -85 dBm
TX
Pout: 16 dBm
5
dBm
19.5
dBm
16
dBm
P1dB
20 dBm
-50
dBm
13.5
dBm
16
dBm
-21
dBm
-26.2
dBm
-28.7
dBm
x2

## Slide 8: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
RX | LNA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB | Voltage= 5 V Current= 55 mA | $ 9.95 | 2
 | Mixer 2.0-2.7 GHz | ADE-R3GLH+ | LO Power: +10 dBm Conversion Loss: 5.2 dB LO-RF Isolation: 35 dB | passive | $ 3.85 | 1
 | BPF 2.3-3.1 GHz | XBF-282+ | Insertion Loss: 2.5 dB Return Loss: 20 dB | passive | $ 10.45 | 1
TX | VCO 2.3-2.5 GHz | ROS-2536C-119+ | Power Output: +6 dBm | Voltage= 5 V Current= 45 mA | $ 18 | 1
 | Splitter | BP2U1+ | Insertion Loss: 3.5 dB | passive | $ 0.96 | 1
 | PA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB P1dB: 19.5 dBm | Voltage= 5 V Current= 55 mA | $ 9.95 | 1

## Slide 9: Received Power Estimation
Target Range (m) | Path Loss (dB) | Power Received (dBm)
5 | 45.02 | -29.02
10 | 51.04 | -35.04
20 | 57.06 | -41.06
40 | 63.09 | -47.09
50 | 65.02 | -49.02