## Slide 1: EEC 134B 2.4 GHz FMCW Radar System
TEAM ONE
2017/03/04

## Slide 2: RF Board
Part 1
Jo Han Yu

## Slide 3: RF Board Testing– with RX Signal from Synx
TX output at 2423.8 MHz
Expected: 14 dBm
Measured: 12.7 dBm
RX input power from synx
2424 MHz with -37.5 dBm
Modify the Arduino code to generate constant 2.45V voltage
Output waveform before filter stage
344 kHz with 3V amplitude
Successfully downcovert and amplify the signal

## Slide 4: RF Board Testing– with Two Coffee Can Antennas
Output waveform is 164.55 Hz with 2.313V Vp-p
Voltage from 0.5V to 3.5V
Freq. from 2300 to 2500 MHz
Use coffee can antennas transmit to a metal cabinet and receive the signal

## Slide 5: RF Board Testing– with Various Antennas
Voltage from 0.5V to 3.5V
Freq. from 2300 to 2500 MHz
With two coffee can antennas
Vp-p = 2.313V
With one coffee can antenna and one
Vp-p = 3.31V

## Slide 6
 | 2.08GHz | 2.51GHz
Distance | Coupling(dB) | 
1 | -26.7 | -22.4
2 | -29.9 | -23
5 | -31 | -37.9
10 | -35.9 | -37.7
15 | -39.7 | -37.1
Chart: Antenna Coupling
| 1 | 2 | 5 | 10 | 15
2.51GHz | -22.4 | -23 | -37.9 | -37.7 | -37.1
2.08GHz | -26.7 | -29.9 | -31 | -35.9 | -39.7
Coupling within frequency range was between -30 to -45 dB after 5 inches.
Is this an issue?
If so solutions?

## Slide 7: Return loss
-10 dB point at 2.07GHz and 2.53GHz
About -21dB at 2.11GHz
About -15dB at 2.2GHz
Gradual decrease to About -20dB at 2.4GHz

## Slide 8: Issues
Unable to get constant 5V from regulator output for RF board
Output waveform is good but when connected to the laptop the waveform disappear