## Slide 1: EEC 134B 2.4 GHz FMCW Radar System
Team One
2017/01/27

## Slide 2: RF Board
Part 1
Jo Han Yu

## Slide 3: RF System Block Diagram
20 kHz Active LPF
TX
RX
Splitter
PA
VCO
BPF
Mixer
LNA

## Slide 4: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
RX | LNA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB | Voltage= 5 V Current= 55 mA | $ 9.95 | 2
 | Mixer 2.0-2.7 GHz | ADE-R3GLH+ | LO Power: +10 dBm Conversion Loss: 5.2 dB LO-RF Isolation: 35 dB | passive | $ 3.85 | 1
 | BPF 2.3-3.1 GHz | XBF-282+ | Insertion Loss: 2.5 dB Return Loss: 20 dB | passive | $ 10.45 | 1
TX | VCO 2.3-2.5 GHz | ROS-2536C-119+ | Power Output: +6 dBm | Voltage= 5 V Current= 45 mA | $ 18 | 1
 | Splitter 1.7-3 GHz | BP2U1+ | Insertion Loss: 3.5 dB | passive | $ 0.96 | 1
 | PA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB P1dB: 19.5 dBm | Voltage= 5 V Current= 55 mA | $ 9.95 | 1

## Slide 5: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
Power | Regulator | LT1962EMS8-5 | Output Current= 300 mA Dropout Voltage= 270mV | Voltage= 6 V Current= 30 uA | $ 3.52 | 1

## Slide 6: Schematics of RF Board
Amplifies already integrated bias matching and stabilization circuits in the chip

## Slide 7: Expected Performance for RF Board
5 dBm
19 dBm
15.5 dBm
Spectrum
Analyzer
13 dBm
USB Synx
-20 dBm
9 dBm
3.8 dBm
Oscilloscope
Supply Voltage: 5 V
Total Current: 210 mA
P1dB
19.5 dBm

## Slide 8: Antenna
Part 2
Alexander Coffman

## Slide 9: Antenna Comparison
 | Yagi Antenna 1 | Patch Antenna | Yagi Antenna 2 | Yagi Antenna 3
Frequency (MHz) | 2400-2490 | 2350-2450 | 2400 | 2150-2600
Gain (dBi) | 14 | 8 | 8.5 | 7
Weight (g) | 230 | N/A | N/A | N/A
Impedance (Ohms) | 50 | 50 | 50 | 50
Price | $ 25 | $ 14.5 | $ 37 | Self-design

## Slide 10: Baseband Board
Part 3
Jinhua Chao

## Slide 11
Components | Part Number | Cost | Number
Amplifier | TL974 | $ 0 | 1
ADC | Sound Card | $ 0 | 
Teensy | Teensy 3.2 | $ 0 | 1
DAC | MCP4921 | $ 0 | 1
Regulator_5V | LT1962 | $ 3.52 | 1
Regulator_2.5V | LT1763 | $ 4.78 | 1
Components List

## Slide 12
Amp & Filter: TL974IN
Teensy
DAC
Regulator
Jinhua_baseband schematic

## Slide 13: Next Step
Use regulator to generate stable +5V and +2.5V
Might add another gain stage (total four stages) in our active LPF
Finish the layout of PCB board by next week

## Slide 14: DSP
Part 4
Haolin Yang

## Slide 15: Information of MCU and expected performance
With the control chip of MK20DX256VLH7 Cortex-M4, the overclockable of Teensy 3.2 is 96 MHz. Flash Memory is 256K and ADC is 12 bit. It also has a SPI ,I2C and CAN Bus.

## Slide 16: The Outline of Programming
The main programming is divided by two main part, including converting real time data into frequency domain with FFT and process the Doppler test by the shift buffer.

## Slide 17: The time-line of signal processing
Week 1 | Dividing the labor and making the plan of signal processing
Week 2 | Familiar with the feature of the launchpad
Week 3 | Realize the FFT transformation using CSS and text the launchpad
Week 4 | Realize the communication of computer and launchpad
Week 5 | Realize the combination with baseband
Week 6 | Realize the combination with antenna
Week 7 | Testing the signal processing and optimize the code
Week 8 | Find the potential downsides and make the progress
Week 9 | Combine the all the component and do the test for the whole system
Week 10 | Modify the downside and write the report of the project

## Slide 18: Week One Report
FFT calculation with assistance of library of Arduino
FFT calculation of math by referring to the code of last quarter
Getting familiar with teensy3.2

## Slide 19: Problem
It is hard to find a way to do the test
Having not found the way to uncode the ready made libraries

## Slide 20: Next Step
Finishing all the project 0 in the Arduino kit to help me to under the structure of teensy
Build up the basic test circuit via referring the lab manuals of last quarter.