## Slide 1: EEC 134B 2.4 GHz FMCW Radar System
TEAM ONE
2017/02/03

## Slide 2: RF Board
Part 1
Jo Han Yu

## Slide 3: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
RX | LNA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB | Voltage= 5 V Current= 55 mA | $ 9.95 | 2
 | Mixer 2.0-2.7 GHz | ADE-R3GLH+ | LO Power: +10 dBm Conversion Loss: 5.2 dB LO-RF Isolation: 35 dB | passive | $ 3.85 | 1
 | BPF 2.3-3.1 GHz | BFCN-2435+ | Insertion Loss: 1.5 dB Return Loss: 20 dB | passive | $ 3.95 | 1
TX | VCO 2.3-2.5 GHz | ROS-2536C-119+ | Power Output: +6 dBm | Voltage= 5 V Current= 45 mA | $ 18 | 1
 | Splitter 1.7-3 GHz | BP2U1+ | Insertion Loss: 3.5 dB | passive | $ 0.96 | 1
 | PA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB P1dB: 19.5 dBm | Voltage= 5 V Current= 55 mA | $ 9.95 | 1

## Slide 4: Components List (Already Placed the Order)
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
Power | Regulator | LT1962EMS8-5 | Output Current= 300 mA Dropout Voltage= 270mV | Voltage= 6 V Current= 30 uA | $ 3.52 | 1
Header | Male pins | S1012E-04-ND | 4 PINS | N/A | $ 0.463 | 10
 | Female pins | S7002-ND | 4 PINS | N/A | $ 0.388 | 10
Connector | SMA | 931-1175-ND | Edge mount | N/A | $ 3.16 | 5
Jumper | Male-Female | 1471-1231-ND | Male to female jumper | N/A | $ 3.06 | 20

## Slide 5: Original RF Board
Cross RF path

## Slide 6: Revised RF Board
Route below GND pad

## Slide 7: Antenna
Part 2
Alexander Coffman

## Slide 8: Yagi Antenna from TI
The Gerber file provided from TI is a 4 layers design.
The price for four-layer fabrication is $ 180.
We would like to consider the back-up solution.

## Slide 9: Backup 1
Gain: 10-11 dBi
Connector: solder the Coax shield to the pad
Price: $5.99 each
We cannot order things from eBay. Department do not use eBay as vendor.
Purchase by ourselves?

## Slide 10: Backup 2
Gain: 8dBi
Connector: RP-SMA Plug (Male)
Dimension: 167.3 x 66 x 18mm
Price: $19.99 each
Thanks to team Radionaughts

## Slide 11: Baseband Board
Part 3
Jinhua Chao

## Slide 12: Next Steps
Wait for PCB coming back and then start assembling
All components are ready

## Slide 13: DSP
Part 4
Haolin Yang

## Slide 14: Week four Report
realize the final DSP on matlab
realize the basic real time signal analysis by using simulink

## Slide 15: Problem
With simulink, I can only draw the plot which show the relationship of two channels.

## Slide 16: Plan for next week
Start to use teensy to do the analysis of digital signal