## Slide 1: EEC 134B 2.4 GHz FMCW Radar System
TEAM ONE
2017/02/03

## Slide 2: RF Board
Part 1
Jo Han Yu

## Slide 3: RF System Block Diagram
20 kHz Active LPF
TX
RX
Splitter
PA
VCO
BPF
Mixer
LNA
BPF

## Slide 4: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
RX | LNA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB | Voltage= 5 V Current= 55 mA | $ 9.95 | 2
 | Mixer 2.0-2.7 GHz | ADE-R3GLH+ | LO Power: +10 dBm Conversion Loss: 5.2 dB LO-RF Isolation: 35 dB | passive | $ 3.85 | 1
 | BPF 2.3-3.1 GHz | BFCN-2435+ | Insertion Loss: 1.5 dB Return Loss: 20 dB | passive | $ 3.95 | 1
TX | VCO 2.3-2.5 GHz | ROS-2536C-119+ | Power Output: +6 dBm | Voltage= 5 V Current= 45 mA | $ 18 | 1
 | Splitter 1.7-3 GHz | BP2U1+ | Insertion Loss: 3.5 dB | passive | $ 0.96 | 1
 | PA 2.3-2.7 GHz | TAMP-272LN+ | Gain:14.5 dB NF: 0.85 dB P1dB: 19.5 dBm | Voltage= 5 V Current= 55 mA | $ 9.95 | 1

## Slide 5: Components List
Function | Components | Part Number | Crucial Specification | Power Consumption | Cost | Number
Power | Regulator | LT1962EMS8-5 | Output Current= 300 mA Dropout Voltage= 270mV | Voltage= 6 V Current= 30 uA | $ 3.52 | 1

## Slide 6: Revised Schematics of RF Board
Amplifies already integrated bias matching and stabilization circuits in the chip

## Slide 7: PCB Layout of RF Board (Top View)
DFM report all PASS
Connectors has aligned to baseband board

## Slide 8: PCB Layout of RF Board (Bottom View)
DFM report all PASS

## Slide 9
RF Board with Baseband Board
Teensy 3.1 and potentiometer are too thick to place between two boards

## Slide 10: Expected Performance for RF Board
Supply Voltage: 6 V
Total Current: 210 mA
5 dBm
19 dBm
15.5 dBm
Spectrum
Analyzer
USB Synx
-20 dBm
9 dBm
7.5 dBm
Oscilloscope
P1dB
19.5 dBm
14 dBm
15.5 dBm
2.3 dBm

## Slide 11: Antenna
Part 2
Alexander Coffman

## Slide 12: Top View

## Slide 13: Bottom View
On DFM Report all Pass

## Slide 14: Backup
Gain: 8dBi
Connector: RP-SMA Plug (Male)
Dimension: 167.3 x 66 x 18mm
Price: $19.99 each
Thanks to team Radionaughts

## Slide 15: Baseband Board
Part 3
Jinhua Chao

## Slide 16
Components | Part Number | Cost | Number
Amplifier | TL974 | $ 0 | 1
ADC | Sound Card | $ 0 | 
Teensy | Teensy 3.2 | $ 0 | 1
DAC | MCP4921 | $ 0 | 1
Regulator_5V | LT1962 | $ 3.52 | 1
Regulator_2.5V | LT1763 | $ 4.78 | 1
Components List

## Slide 17: Schematics of baseband Board
Add an test pin after gain stage

## Slide 18: PCB Layout of RF Board (Top View)
DFM report all PASS
Connectors has aligned to RF board

## Slide 19: PCB Layout of RF Board (Bottom View)
DFM report all PASS

## Slide 20: Testing set up
DAC
TX
RX
Function Generator
PA
Input the sinusoid wave with frequency from low to high
The output of high frequency input will be distorted
3.2

## Slide 21: DSP
Part 4
Haolin Yang

## Slide 22: Week Three Report
Confirm the DAC output of Teensy3.2
Collect the wave data with soundcard by audiocity and MATLAB
Testing the code of FFT

## Slide 23: Issues
When using MATLAB to collect the wave data, encountering the problem of noise
Cannot generate the RTI plot

## Slide 24: Plan for next week
Dealing with the problem of RTI Plot
Realize the real time analysis to make sure the basic requirement for the final competition to minimize the risk of failure to use teensy to do the DSP.